## Slide 1: Small-scale Mobile radio propagation
Small scale propagation implies signal quality in a short distance or time range
In this small range, fading or rapid fluctuation of the signal amplitude is observed
One cause of fading is multipath or the process of signals reaching the receiver through different mechanisms such as LOS, reflection, diffraction and scattering.

## Slide 2: Multipath effects
Rapid changes in signal amplitude over a small distance or time interval.
Rapid changes in signal phaseover a small distance or time interval.
Time dispersion (echoes) caused by multipath propagation delay.

## Slide 3: Causes of fading
In urban areas, fading occurs because the height of mobile is lesser than the height of surrounding structures, such as buildings and trees.
Existence of several propagation paths between transmitter and receiver.

## Slide 4: Factors influencing small signal fading
Multipath propagations
Speed of mobile (Doppler shift)
Speed of surrounding objects
Bandwidths of signal and channel

## Slide 5: Analysis of multipath channel
Receiver
d
Spatial position
Transmitter

## Slide 6: Convolution model for multipath signal
Received signal:
y(t) = A0 x(t) + A1 x(t - t 1) + A2 x(t - t 2) + ...
R, y(t)
T
A2 x(t- t 2)
A1 x(t- t 1)
, x(t)
LOS

## Slide 7: System definition of multipath
h(t)
x(t)
y(t)

## Slide 8: Baseband signal definition
x(t) = c(t) cos (2  fct )
Transmitted signal
c(t)- pulse
Received signal
y(t) = r(t) cos (2  fct )

## Slide 9: Base band equivalent channel
hb(t)
c(t)
r(t)

## Slide 10: Modeling of the baseband multipath model
r(t) = c(t) * hb(t, t)
hb(t,t)
t3
t2
t1
t0
t N-2 t N-1
t o t 1 t 2
Mathematical model

## Slide 11: Excess delay concept
The delay axis t, t o<= t <= t n-1 is divided into equal time delay segments called excess delay bins.
t 0 = 0
t 1 =  t
t 2 = 2  t
t N-1 = (N-1) t

## Slide 12: Delay component design
All multipath signals received within the bins are represented by a single resolvable multipath component having delay t i .
Design equation for bin width t:
      Bandwidth of signal = 2/t

## Slide 13: Final model for multipath response
N-1 j i
r(t) =  ai e c[t –ti]
i = 0
c(t) – Transmitted pulse
r(t) – Received pulse
N – Number of multipaths
ai – Amplitude of multipath i
qi – Phase of multipath i
ti – Time delay of multipath i

## Slide 14: Wideband multipath signals
N-1 j  i
Received signal r(t) =  ai e p[t–ti]
i = 0
Instantaneous received power:
N-1
|r(t)|2 =  |ak|2
k = 0
=>Total received power = sum of the power of individual multipath components.

## Slide 15: Narrowband multipath signals
N-1 ji
Received signal: r(t) =  ai e p[t–ti]
i = 0
Instantaneous received power:
N-1 ji
    |r(t)|2 = |  ai e |2
i = 0

## Slide 16: Conclusions
When the transmitted signal hasa wide bandwidth >> bandwidth of the channel, multipath structure is completely resolved by the receiver at any time and the received power varies very little.
When the transmitted signal has a very narrow bandwidth (example the base band signal has a duration greater than the excess delay of the channel) then multipath is not resolved by the received signal and large signal fluctuations occur (fading).

## Slide 17: Example
Assume a discrete channel impulse response is used to model urban radio channels with excess delays as large as 100 s and microcellular channels with excess delays not larger than 4 s. If the number of multipath bins is fixed at 64 find:
(a)  t
(b) Maximum bandwidth, which the two models can accurately represent.

## Slide 18: Solution
For urban radio channel
Maximum excess delay of channel
t N = N t = 100  s.
N = 64
t = tN /N = 100 s /64 = 1.5625 s
Maximum bandwidth represented accurately by model
= 2/ t = 1.28 MHz

## Slide 19: For microcellular channel
Maximum excess delay of channel
t N = N t = 4  s.
N = 64
t = t N /N = 4  s /64 = 62.5 ns
Maximum bandwidth represented accurately by model =
2/ t = 32 MHz

## Slide 20: Small-scale multipath measurements
Direct Pulse Measurements
Spread Spectrum Sliding Correlator Measurement
Swept Frequency Measurement

## Slide 21: Types of Small Scale Fading
Multipath time delay
Doppler Spread
Flat fading
Frequency
Selective
Fading
Fast
Fading
Slow fading

## Slide 22: Mechanisms that cause fading
2 main propagation mechanisms:
  Multipath time delay spread
  Doppler spread
These two mechanisms are independent of each other.

## Slide 23: Multipath terms associated with fading
Ts = Symbol period or reciprocal bandwidth
Bs = Bandwidth of transmitted signal
Bc = Coherence bandwidth of channel
Bc= 1/(50)where  is rms delay spread

## Slide 24: Calculation of Delay Spread
__ _
 2 =  2 - ( )2
Where:
_
 = ( ak2 ) / ( ak2)
__
 2 = ( ak2 2) / ( ak2)

## Slide 25: Fading effects due to Doppler spread
fc = frequency incident signal
Received signal spectrum = fc +/- fd
fd = Doppler shift
fc

V

## Slide 26: Doppler spread and coherence time
Doppler frequency shift : fd = (v / ) cos  ,
Wavelength  = c / fc
Maximum Frequency deviation = fm = v / 
Doppler Spread BD = fm
Coherence time = Tc = 0.423 / fm

## Slide 27: Mathematical estimation of fading
Flat fading
Most common type of fading
Spectral characteristics of the transmitted signal are maintained at receiver
Condition:
Bs << Bc
=> Ts >> 

## Slide 28
Frequency selective fading
Due to time dispersion of transmitted symbols within the channel
Received signal undergoes distortion
Condition:
Bs > Bc
=> Ts < 

## Slide 29: Flat fading or frequency selective fading?
Common rule of thumb
If Ts ≥ 10  => Flat fading
If Ts < 10  => Frequency selective fading

## Slide 30: Fast fading channel
The channel impulse response changes rapidly within the symbol duration.
This causes frequency dispersion due to Doppler spreading, which leads to signal distortion.
Condition:
Ts > Tc
Bs < BD

## Slide 31: Slow fading channel
The channel impulse response changes at a much slower rate than the transmitted signal
Velocity of mobile (or velocity of objects in channel)
Condition:
Ts < Tc
Bs > BD

## Slide 32: Rayleigh and Ricean distributions
In mobile radio channels, the Rayleigh distribution is commonly used to describe the statistical time varying nature of the received fading signal
When there is a dominant (non-fading) signal component present such as LOS propagation path, the small scale fading envelope distribution is Ricean

## Slide 33: Level crossing and fading statistics
Level crossing rate (LCR)
  Rate at which the normalized Rayleigh fading envelope crosses a specified level in a positive going direction.
LCR = NR = (2) fm e-2
fm = Maximum Doppler frequency
 = R/Rms = specified level R, normalized to the rms value of fading signal

## Slide 34: Average fade duration
  Average period of time for which the received signal is below a specified level R.
__
 = e2– 1
________
fm2

## Slide 35: Example
(a) For a Rayleigh fading signal, compute the positive going level crossing rate for  = 1, when the maximum Doppler frequency, fm, is 20 Hz.
(b) What is the average fade duration?

## Slide 36: Solution
 = 1
fm = 20 Hz
(a) Number of zero level crossings is:
NR = 2 (20) e-1
= 18.44 Crossings/Sec
Maximum velocity of mobile
= fd  = 20 (3 X 108)/(900X106)
= 6.66 m/s

## Slide 37
(b) Average fade duration
__
 = e2– 1
________
fm2
= e1– 1
________ = 0.034 s
1x 202p

## Slide 38: Statistical methods for fading channels
Clark’s model for Flat Fading
Two-Ray Rayleigh Fading Model
Saleh and Valenzuela Indoor statistical Model
SIRCIM (Simulation of Indoor Radio Channels Impulse Response Models)
SMRCIM (Simulation of Mobile Radio Channel Impulse-Response Models)