## Slide 1: Modulation Techniques for Mobile Radio
Modulation is the process of encoding the baseband or source information (voice, video, text) in a manner suitable for transmission.
It generally involves translating a baseband signal (or source) to a band pass signal, centered at a high carrier frequency.
Demodulation is the process of extracting the baseband message from the carrier.

## Slide 2: Modulation Techniques
Modulation
Analog Modulation
(First Generation (1G) Mobile Radio)
Digital Modulation
(2G, 3G, 4G, 5G systems)

## Slide 3: Review of Analog Modulation Techniques
Amplitude Modulation (AM)
Message Signal --
Carrier Signal --
AM Signal --

## Slide 4: Single Singleband AM Signal
Lower Sideband
Upper Sideband
Where the Hilbert transform is defined as:
;

## Slide 5: Balanced Modulator
Carrier fc
-90o phase shift
90o
∑

## Slide 6: Properties of SSB
Bandwidth of SSB is very efficient = fm (half of AM bandwidth)
However, Doppler spreading and Rayleigh fading can shift the signal spectrum, causing distortion.
Frequency of the receiver oscillator must be exactly the same as that of the transmitted carrier fc. If not, this results in a frequency shift fc f, causing distortion.

## Slide 7: Pilot Tone SSB
Transmit a low level pilot tone along with the SSB signal.
The pilot tone has information on the frequency and amplitude of the carrier.
The pilot tone can be tracked using signal processing FFSR - Feed Forward Signal Regeneration.

## Slide 8: Properties of TTIB system
Base band signal is split into two equal width segments.
Small portion of audio spectrum is removed and a low-level pilot tone is inserted in its place.
This procedure maintains the low bandwidth of the SSB signal.
  Provides good adjacent channel protection.

## Slide 9: Demodulation of AM signals
Coherent Modulation
Non-coherent demodulation
Envelope Detectors

## Slide 10: Frequency Modulation
Message Signal –
FM Signal –
Power in FM Signal –
Bandwidth of FM >> Bandwidth of AM (hence higher quality in audio, music)

## Slide 11: FM methods
FM Modulation
Direct Method – VCO
Indirect Method – Armstrong
FM Detection
Slope Detection
Zero Crossing Detection
PLL Detection
Quadrature Detection

## Slide 12: Comparison between AM and FM
FM | AM
FM signals are less noisy, because amplitude of signal is constant | AM signals are more noisy, amplitude cannot be limited
The modulation index can be varied to obtain greater SNR(6dB for each doubling in bandwidth) | Modulation index cannot be changed automatically.
FM signals occupy more bandwidth (good for audio) | AM signals occupy lesser bandwidth (good for video)

## Slide 13: Digital Modulation
VLSI and DSP promoted the advent of Digital Modulation
Low noise
Easier multiplexing of information (voice, data, video)
Can accommodate digital transmission errors, source coding, encryption and equalization.
DSP can implement digital modulators, demodulators completely in software.

## Slide 14: Basics of digital communications
In digital communication systems, the message) is represented as a time sequence of symbols or pulses.
Each symbol has m finite states
Number of bits required for m states:
  n = log2m bits/symbol

## Slide 15: Shannon’s bandwidth theorem
Shannon's formula:
Channel capacity C= Maximum bit rate
C = B log2(1 + S/N)
S/N = Signal to Noise ratio
B = Channel bandwidth

## Slide 16
Practical digital systems
For US digital cellular standard, R = 48.6 kbps
RF bandwidth = 30 KHz
For SNR 20 dB => 100
C = 30000 * log2(1 + S/N)
= 30000 * log2(1 + 100) = 199.75 kbps
For GSM standard, R = 270.833 kbps
C = 1.99 Mbps for S/N = 30 dB

## Slide 17: Line Coding
Line codes are used to convert bits into voltages.
Line codes provide the pulses to represent 0s and 1s.
Line codes can be:
  Return-to-zero (RZ)
  Non-return-to-zero (NRZ)
Line codes are Unipolar (0,V) or Bipolar (-V, V )

## Slide 18: Unipolar NRZ 1 0 1 1 0
V
0 Unipolar RZ
V Bipolar NRZ
-V

## Slide 19: Pulse Shaping Techniques
ISI – Inter Symbol Interference  Due to sharp edges in rectangular pulses
Pulse shaping techniques reduce the inter-symbol effects
Bandlimited
Channel

## Slide 20: Pulse shaping filters
Raised cosine filter
As the value of a (roll-off factor) increases, the bandwidth of the filter also increases
As the value of a (roll-off factor) increases, the time sidelobe levels decrease.

## Slide 21: Symbol rate with raised-cosine filter
Symbol rate possible through raised cosine filter
where B is the filter bandwidth

## Slide 22: Types of Digital Modulation
Linear | Non-Linear | Spread Spectrum
Amplitude of transmitted signal varies linearly with message signal m(t) | Amplitude of carrier is constant | Transmission bandwidth >> signal bandwidth
Low bandwidth- allows more users | High bandwidth –Low noise | More users-high bandwidth
Example systems: BPSK, QPSK | FSK, GMSK | W-CDMA, cdma2000

## Slide 23: Linear digital modulation
PSK or Phase Shift Keying of carrier:
SPSK = A cos(wt + fk)
fk = 0, p (BPSK)
fk = 0, p/2, p, 3p/2 (QPSK)
fk = 0,p/4,p/2,3p/4,p,5p/4,3p/2,7p/4 (0PSK)

## Slide 24: Properties of PSK
BPSK
BW = 2 RB = 2 / TB
Pe,BPSK = Q[√(2 EB / N0)]
RB – Bit rate, TB – Bit period
EB /N0 – SNR
QPSK
BW = RB = 1 / TB
Pe,QPSK = Q[√(2 EB / N0)]

## Slide 25: Nonlinear digital modulation
Frequency shift keying
The frequency of a constant amplitude carrier signal is switched between 2 values ( 1 and 0)

## Slide 26: Properties of FSK
Transmission Bandwidth
BT = 2f + 2B
B = Bandwidth of digital base-band signal
If a raised cosine pulse-shaping filter is used
BT = 2f + (1 + )R
Probability of error
Pe,FSK = Q[(EB / N0)1/2]

## Slide 27: Modulation performance in fading channels
s(t) r(t)
r(t) = (t) e-j(t) s(t) + n(t)
(t) = gain of the channel
(t) = phase shift of the channel
n(t) = additive Gaussian noise
Fading Channel

## Slide 28: BER with noise and fading
SNR (with fading) G = a2 Eb/No
PSK
FSK

## Slide 29: Spread Spectrum Modulation techniques
Spread spectrum techniques employ a transmission bandwidth >> signal bandwidth
The system is inefficient for a single user, but is efficient for many users
Many users use the same bandwidth without significantly interfering with one another

## Slide 30: Principle of Spread Spectrum
Spread spectrum signals are PN (pseudo – noise) sequence or code.
Spread spectrum signals are demodulated at the receiver by cross correlation with the correct PN sequence.
PN codes are approximately orthogonal, and the receiver can separate each user based on their codes.

## Slide 31: Advantages of spread spectrum techniques
Spread spectrum communications (3G) offer high bandwidth compared to 1G and 2G systems.
Resistance to multi-path fading, because of large bandwidths and narrow time widths.

## Slide 32: PN Sequences
Pseudo Noise sequence is a binary sequence of 1s and -1s
PN sequences are generated by using sequential logic circuits
PN sequence is unique for each user and allows users to share bandwidth without interference

## Slide 33: Frequency Hopped Spread spectrum (FHSS)
A frequency hopping signal periodically changes the carrier frequency by using PN control
The set of possible carrier frequencies is called a hopset
Hit => Two users using the same frequency band at the same time
Bandwidth of channel  B
Bandwidth of spectrum  total bandwidth Wss

## Slide 34: Methodology of FHSS
Time duration between hops  hopping period Ts
Data is sent by hopping the transmitter carrier over the hopset generated by PN codes
Small bursts of data are sent before T/R hops again
Hit => Two users using the same frequency band at the same time

## Slide 35: Frequency Hopping Modulator
Modulator
PN Code
Generator
Frequency
Synchronizer
Code Block
DATA
Frequency
Hopping
Signal
Oscillator

## Slide 36: Frequency hopping demodulator
Wideband
Filter
PN Code
Generator
Frequency
Synthesizer
Synchronization
System
BP Filter
Demodulation
DATA
Frequency
Hopping
Signal

## Slide 37: Parameters of FH-SS
Probability of error for BPSK Spread Spectrum
Pe = 0.5 x e -Eb/ 2N0 x (1 – ph ) + 0.5 ph
ph = probability of hit = 1 – (1 – 1/M)K-1
M = number of hopping channels
K = Total number of users
Processing gain (PG) = Wss / B

## Slide 38: Direct Sequence Spread Spectrum (DSSS)
code
time
frequency
C1
C2
CN

## Slide 39: Properties of DSSS signal
Message signal is a time sequence of non-overlapping pulses of duration T, each of which has an amplitude (+/-) 1.
The PN waveform consists of N pulses or chips for message symbol period T.
NTC = T
where TC is the chip period.

## Slide 40: Example:
N=4
PN Wave for N =4
1
-1
-1
1

## Slide 41: DSSS Transmitter

1
k
mk(t)

## Slide 42: CDMA Receiver
(.)dt



## Slide 43: Parameters of DSSS
Probability of bit error (BER)
Pe = Q {1/ [(K –1)/3N + (N0/2Eb)]1/2}
K = Number of users
N = Number of chips/ symbol

## Slide 44: Important Advantages of CDMA
Many users of CDMA use the same frequency
Multipath fading may be substantially reduced because of large signal bandwidth.
There is no absolute limit on the number of users in CDMA
System performance gradually degrades for all users as the number of users is increased.

## Slide 45: Drawbacks of CDMA
Self-jamming is a problem in a CDMA system. Self-jamming occurs because the PN sequences are not exactly orthogonal.
The near- far problem occurs at a CDMA receiver if an undesired user has high detected power as compared to the desired user.