DRAFT*

*For the final version, I may add some things but I won’t take anything off except perhaps irrelevant data.

Information and Formulas (Ex1, F04)

## Atomic Weights and Ion Charges of Selected Elements

| H+ | 1 | Na+ | 23 | S | 32 | Fe2+ or Fe 3+ | 55.8 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C | 12 | Mg2+ | 24.3 | Cl- | 35.5 | Cu2+ | 63.5 |
| N | 14 | Al3+ | 27 | K+ | 39.1 | Zn2+ | 65.4 |
| O | 16 | P | 31 | Ca2+ | 40 | Pb2+ | 207.2 |

Conversion Factors and Constants

Gas constant = 0.08205 atm L / mole K

| 7.48 gal/ft3 | 3.785 L/gal | 2.205 lb/kg | 43,560 ft2/ac | 1000 L/m3 | 1 mg/L = 1 g/m3 |
| --- | --- | --- | --- | --- | --- |
| 62.4 lb/ft3, H2O | 3.28 ft/m | 454 gram/lb | 104 m2/ha | 273(K = 0(C |  |

Henry’s Law Constants. HA x 10-4 (atm)

| Temp (C | Air | CO2 | N2 | O2 | CH4 |
| --- | --- | --- | --- | --- | --- |
| 0 | 4.32 | 0.0728 | 5.29 | 2.55 | 2.24 |
| 10 | 5.49 | 0.104 | 6.68 | 3.27 | 2.97 |
| 20 | 6.64 | 0.142 | 8.04 | 4.01 | 3.76 |

Henry’s Law Constants, KH (atm/M) all at 25 (C

| Benzene | 5.6 | DDT | 0.038 |
| --- | --- | --- | --- |
| Phenol | 0.00076 | Chloroform | 4.1 |

Solubility Products, Ks at 25 (C

| CaCO3 | 4.95x10-9 | FeS | 1.57x10-19 |
| --- | --- | --- | --- |
| Ca(OH)2 | 7.88x10-6 | Pb(OH)2 | 1.40x10-20 |
| Cu(OH)2 | 2.0x10-19 | Mg(OH)2 | 1.82x10-11 |
| Fe(OH)3 | 2.67x10-39 | MgCO3 | 1.15x10-5 |

Acid Dissociation Constants, pK values

| Carbonic acid (H2CO3) | 6.35 | 10.33 |
| --- | --- | --- |
| Acetic acid (HA) | 4.75 |  |
| Hydrogen sulfide (H2S) | 7.2 | 11.89 |
| Hypochlorous acid (HOCl) | 7.54 |  |
| Ammonium (NH4+) | 9.3 |  |
| Hydrocloric acid (HCl) | -3 |  |